## Slide 1: SFS: Random Write Considered Harmful in Solid State Drives
Changwoo Min1, 2, Kangnyeon Kim1, Hyunjin Cho2, Sang-Won Lee1, Young Ik Eom1
1Sungkyunkwan University, Korea
2Samsung Electronics, Korea

## Slide 2: Outline
Background
Design Decisions
Introduction
Segment Writing
Segment Cleaning
Evaluation
Conclusion

## Slide 3: Flash-based Solid State Drives
Solid State Drive (SSD)
  A purely electronic device built on NAND flash memory
  No mechanical parts
Technical merits
  Low access latency
  Low power consumption
  Shock resistance
  Potentially uniform random access speed
Remaining two problems limiting wider deployment of SSDs
  Limited life span
  Random write performance

## Slide 4: Limited lifespan of SSDs
Limited program/erase (P/E) cycles of NAND flash memory
  Single-level Cell (SLC): 100K ~ 1M
  Multi-level Cell (MLC): 5K ~ 10K
  Triple-level Cell (TLC): 1K
As bit density increases
   cost decreases, lifespan decreases
Starting to be used in laptops, desktops and data centers.
  Contain write intensive workloads

## Slide 5: Random Write Considered Harmful in SSDs
Random write is slow.
  Even in modern SSDs, the disparity with sequential write bandwidth is more than ten-fold.
Random writes shortens the lifespan of SSDs.
  Random write causes internal fragmentation of SSDs.
  Internal fragmentation increases garbage collection cost inside SSDs.
  Increased garbage collection overhead incurs more block erases per write and degrades performance.
  Therefore, the lifespan of SSDs can be drastically reduced by random writes.

## Slide 6: Optimization Factors
SSD H/W
  Larger over-provisioned space  lower garbage collection cost inside SSDs
  Higher cost
Flash Translation Layer (FTL)
  More efficient address mapping schemes
  Purely based on LBA requested from file system
    Less effective for the no-overwrite file systems
  Lack of information
Applications
  SSD-aware storage schemes (e.g. DBMS)
  Quite effective for specific applications
  Lack of generality
SSD H/W
Flash Translation Layer
(FTL)
File System
Applications
We took a file system level approach to directly exploit file block level statistics and provide our optimizations to general applications.

## Slide 7: Outline
Background
Design Decisions
  Log-structured File System
  Eager on writing data grouping
Introduction
Segment Writing
Segment Cleaning
Evaluation
Conclusion

## Slide 8: Performance Characteristics of SSDs
If the request size of the random write are same as erase block size, such write requests invalidate whole erase block inside SSDs.
Since all pages in an erase block are invalidated together, there is no internal fragmentation.
The random write performance becomes same as sequential write performance when the request size is same as erase block size.

## Slide 9: Log-structured File System
How can we utilize the performance characteristics of SSD in designing a file system?
Log-structured File System
  It transforms the random writes at file system level into the sequential writes at SSD level.
  If segment size is equal to the erase block size of a SSD, the file system will always send erase block sized write requests to the SSD.
  So, write performance is mainly determined by sequential write performance of a SSD.

## Slide 10: Eager on writing data grouping
To secure large empty chunk for bulk sequential write, segment cleaning is needed.
  Major source of overhead in any log-structured file system
  When hot data is colocated with cold data in the same segment, cleaning overhead significantly increases.
1
2
3
4
5
6
7
8
1
3
7
8
2
4
5
6
Traditional LFS writes data regardless of hot/cold and then tries to separate data lazily on segment cleaning.
  If we can categorize hot/cold data when it is first written, there is much room for improvement.
   Eager on writing data grouping
Disk segment (4 blocks)
1
3
7
8
Four live blocks should be moved to secure an empty segment.
1
3
7
8
No need to move blocks to secure an empty segment.

## Slide 11: Outline
Background
Design Decisions
Introduction
Segment Writing
Segment Cleaning
Evaluation
Conclusion

## Slide 12: SFS in a nutshell
A log-structured file system
Segment size is multiple of erase block size
  Random write bandwidth = Sequential write bandwidth
Eager on writing data grouping
  Colocate blocks with similar update likelihood, hotness, into the same segment when they are first written
  To form bimodal distribution of segment utilization
  Significantly reduces segment cleaning overhead
Cost-hotness segment cleaning
  Natural extension of cost-benefit policy
  Better victim segment selection

## Slide 13: Outline
Background
Design Decisions
Introduction
Segment Writing
Segment Cleaning
Evaluation
Conclusion

## Slide 14: On Writing Data Grouping
Colocate blocks with similar update likelihood, hotness, into the same segment when they are first written.
1
Dirty Pages: t
2
3
4
5
6
1. Calculate hotness
1
2
3
4
5
6
2. Classify blocks
1
3
4
5
2
6
Hot group
Cold group
3. Write large enough groups
1
3
4
5
Disk segment (4 blocks)
2
6
Dirty Pages: t+1
How to measure hotness?
How to determine grouping criteria?

## Slide 15: Measuring Hotness
Hotness: update likelihood
  Frequently updated data  hotness ↑
  Recently updated data  hotness ↑
File block hotness Hb | Segment hotness Hs
File block hotness Hb | Segment hotness Hs

## Slide 16: Determining Grouping Criteria : Segment Quantization
equi-width partitioning
The effectiveness of block grouping is determined by the grouping criteria.
  Improper criteria may colocate blocks from different groups into the same segment, thus deteriorates the effectiveness of grouping.
Naïve solution does not work.
hot group
warm group
cold
group
read-only
group
equi-height partitioning
hot group
warm group
cold group
read-only group

## Slide 17: Iterative Segment Quantization
Find natural hotness groups across segments in disk.
  Mean of segment hotness in each group is used as grouping criterion.
  Iterative refinement scheme inspired by k-means clustering algorithm
Runtime overhead is reasonable.
  32MB segment  only 32 segments for 1GB disk space
  For faster convergence, the calculated centers are stored in meta data and loaded at mounting a file system.
Randomly select initial center of groups
Assign each segment to the closest center.
Calculate a new center by averaging hotnesses in a group.
Repeat Step 2 and 3 until convergence has been reached or three times at most.

## Slide 18: Process of Segment Writing
Writing of the small groups will be deferred until the size of the group grows to completely fill a segment.
Eventually, the remaining small groups will be written at creating a check-point.
Segment Writing
2. Classify dirty blocks according to hotness
warm
blocks
hot
blocks
read-only
blocks
cold
blocks
3. Only groups large enough to completely fill a segment are written.
1. Iterative segment quantization
write request
Segment writing is invoked in four case:
every five seconds
flush daemon to reduce dirty pages
segment cleaning
sync or fsync

## Slide 19: Outline
Background
Design Decisions
Introduction
Segment Writing
Segment Cleaning
Evaluation
Conclusion

## Slide 20: Cost-hotness Policy
Natural extension of cost-benefit policy
In cost-benefit policy, the age of the youngest block in a segment is used to estimate update likelihood of the segment.
  cost-benefit
In cost-hotness policy, we use segment hotness instead of the age, since segment hotness directly represents the update likelihood of segment.
  cost-hotness
  Segment cleaner selects a victim segment with maximum cost-hotness value.

## Slide 21: Writing Blocks under Segment Cleaning
Live blocks under segment cleaning are handled similarly to typical writing scenario.
  Their writing can also be deferred for continuous re-grouping
  Continuous re-grouping to form bimodal segment distribution.

## Slide 22: Scenario of Data Loss in System Crash
There are possibility of data loss for the live blocks under segment cleaning in system crash or sudden power off.
1
3
7
8
1
2
3
4
disk segment
1
3
7
8
2
4
dirty pages
1
2
3
4
2
4
1. Segment cleaning. Live blocks are read into the page cache.
1
2
3
4
2
4
1
3
7
8
2
4
1
3
7
8
2. Hot blocks are written.
3. System Crash!!
 Block 2, 4 will be lost since they do not have on-disk copy.

## Slide 23: How to Prevent Data Loss
Segment Allocation Scheme
  Allocate a segment in Least Recently Freed (LRF) order.
Check if writing a normal block could cause data loss of blocks under cleaning.
This guarantees that live blocks under cleaning are never overwritten before they are written elsewhere.
disk segment
1
3
7
8
2
4
dirty pages
1
2
3
4
1
2
3
4
2
4
St: currently allocated segment
St+1: segment that will be allocated next time
1. Check if live blocks under cleaning is originated from St+1?
1
2
3
4
1
2
3
4
2
4
St: currently allocated segment
St+1: segment that will be allocated next time
1
3
7
8
2
4
2. If so, write the live blocks under cleaning first regardless of grouping.
2
4
1
3
7
8
`
`
`
`

## Slide 24: Outline
Background
Design Decisions
Introduction
Segment Writing
Segment Cleaning
Evaluation
Conclusion

## Slide 25: Evaluation
Server
  Intel i5 Quad Core, 4GB RAM
  Linux Kernel 2.6.37
SSD
Configuration
  4 data groups
  Segment size: 32MB
 | SSD-H | SSD-M | SSD-L
Interface | SATA | SATA | USB 3.0
Flash Memory | SLC | MLC | MLC
Max. Sequential Writes (MB/s) | 170 | 87 | 38
Random 4KB Writes (MB/s) | 5.3 | 0.6 | 0.002
Price ($/GB) | 14 | 2.3 | 1.4

## Slide 26: Workload
Synthetic Workload
  Zipfian Random Write
  Uniform Random Write
    No skewness  worst-case scenario of SFS
Real-world Workload
  TPC-C benchmark
  Research Workload (RES) [Roseli2000]
    Collected for 113 days on a system consisting of 13 desktop machines of research group.
Replaying workload
  To measure the maximum write performance, we replayed write requests in the workloads as fast as possible in a single thread and measured throughput at the application level.
  Native Command Queuing (NCQ) is enabled.

## Slide 27: Throughput vs. Disk Utilization
* SSD-M
Zipfian Random Write
TPC-C
2x
1.9x
1.7x
2.5x
Uniform Random Write
RES
1.4x
1.2x
1.9x
1.2x

## Slide 28: Segment Utilization Distribution
* Disk utilization is 70%.
Zipfian Random Write
TPC-C
Uniform Random Write
RES
nearly full
nearly empty

## Slide 29: Comparison with Other File Systems
File System
FTL Simulator
workload
Ext4
  In-place-update file system
Btrfs
  No overwrite file system
 Measured Throughput
blktrace
  Coarse grained hybrid mapping FTL
    FAST FTL [Lee’07]
  Full page mapping FTL
   Measured Write Amplification and Block Erase Count

## Slide 30: Throughput under Different File Systems
* Disk utilization is 85%. / SSD-M
1.6x
7.3x
1.5x
1.3x
10.6x
1.3x
2x
14.6x
1.6x
1.4x
48x
2.4x
1.7x
4.2x
1.3x

## Slide 31: Block Erase Count
Coarse Grained Hybrid Mapping FTL: FAST FTL
1.4x
6.7x
4.3x
1.1x
6.4x
2.5x
1.2x
4.9x
2.6x
1.2x
5.4x
Full page mapping FTL
1.3x
7.5x
2.6x
1.1x
2.7x
1.3x
1.2x
2.4x
1.5x
1.2x
2.8x
3.3x
* Disk utilization is 85%.
1.2x
6.1x
3.1x
5.2x
1.2x
3.8x
1.8x

## Slide 32: Outline
Background
Design Decisions
Introduction
Segment Writing
Segment Cleaning
Evaluation
Conclusion

## Slide 33: Conclusion
Random write on SSDs causes performance degradation and shortens the lifespan of SSDs.
We present a new file system for SSD, SFS.
  Log-structured file system
  On writing data grouping
  Cost-hotness policy
We show that SFS considerably outperforms existing file systems and prolongs the lifespan of SSD by drastically reducing block erase count inside SSD.
Is SFS also beneficial to HDDs?
  Preliminary experiment results are available on our poster!

## Slide 34: Thank you! Questions?